Extreme Ultraviolet Normal-Incidence Spectrograph (EUNIS)
Richard Schaefer

---
What is EUNIS?
EUNIS, the Extreme Ultraviolet Normal Incidence Spectrograph, is a sensitive, two-channel spectrograph that measures ultraviolet emission from the solar corona on board a sounding rocket.

---
The Instrument
[Speaker Notes: Go through this faster]

---
Quick Stats
- Two channels
  - 170-205 Å
  - 300-370 Å
- 110 mm diameter telescope
- 3600 grooves/mm grating
- ~2 second cadence
- Spectral resolution up to 35 mÅ
- Most sensitive solar EUV spectrograph
[Speaker Notes: Don't read off the stats]

---
EUNIS Objectives
- To probe the structure and dynamics of the inner solar corona
- To obtain spectra with a cadence as short as 2 sec, allowing unprecedented studies of the physical properties of evolving and transient structures.
- To study diagnostics of wave heating and reconnection at heights above 2 solar radii, in the wind acceleration region.
- To help recalibrate several orbital instruments, including SOHO/CDS and EIT,TRACE, Solar-B/EIS, SDO, and STEREO/EUVI.
  - “Dumbbell” slits
[Speaker Notes: Don't read word for word, summarize quickly]

---
The Coronal Heating Problem
- Rapid rise from ~10^4 K to ~10^6 K
- Magnetic reconnection vs. wave heating
- Nanoflares?
Courtesy Adrian Daw
[Speaker Notes: The main point is that the temperature of the solar atmosphere increases as you move away from the surface. Not something you expect from equilibrium thermodynamics. Not how heat conducts, we know this from the second law of thermodynamics. The diagram is what you would expect from old models]

---
What are spectra?
- Separation of light into distinct frequencies or wavelengths.
- Signature of an atomic transition
- Early evidence for quantum mechanics
- E = hf = hc/λ
[Speaker Notes: Talk about how the many things we are able to discern from the spectra: - chemical composition - temperature - density - motions, translational and rotational - magnetic fields]

---
The Data
[Speaker Notes: Note this is one particular exposure from about 250 Explain horizontal and vertical axes]

---
The Data
MgIX at 368 Ångstroms: A magnesium atom with 8 electrons stripped away. Forms at high temperatures.
[Speaker Notes: Mention how MgIX is an atom with 8 electrons stripped Mention how we know the temperature by the ion which is formed. Note the odd convention that astronomers use.]

---
The Data
[Speaker Notes: Point out how the graph actually corresponds to the spectrum]

---
The Data
- Able to calculate properties of the “stuff” we're looking at, such as
- Intensity = 1.064 * (Amplitude) * (FWHM)
- Velocity = (Δλ/λ)*c
Courtesy hlabsoft.com
[Speaker Notes: Explain what intensity and velocity actually are]

---
Raster Images
Courtesy Jeff Brosius

---
Raster Images
[Speaker Notes: Explain program in general here]

---
Raster Images
[Speaker Notes: Note how you can now compare these side by side]

---
Raster Images

---
Raster Images

---
Raster Images

---
Raster Images

---
Raster Images

---
Quiet Sun :(

---
What I learned
- What spectra are
- Physics
  - Quantum
  - Atomic
  - Astro
  - Plasma
- IDL
- Data reduction

---
What I Learned
⇔

---
Future
- Make GUI for program
- Continue to analyze data
  - Look at short wavelength channel
  - Hope for interesting results

---
Thank You
- Jeff Brosius
- Doug Rabin
- Pat Haas
- Adrian Daw
- Fred Bruhweiler